## Slide 1: T1S 100BASE-T Bridge
Layer 2 Bridge Firmware for ATSAME54P20A
Microchip Technology
2026-08

## Slide 2: Part 1: Architecture & Hardware

## Slide 3: Hardware Platform Overview
Microcontroller — SAM E54P20A
Network Interfaces
• Cortex-M4 core, 120 MHz
• 256 KB SRAM (heap + stack)
• Integrated Ethernet MAC (GMAC)
• SPI interface (CS=PC15, INT=PC14)
• UART via EDBG probe for CLI
• Emulated EEPROM for persistent config
• eth0: LAN8651 PHY (10BASE-T1S)
  – Single-pair Ethernet (point-to-point)
  – PLCA collision avoidance built-in
• eth1: LAN8740A PHY (100BASE-T)
  – Multi-pair Ethernet (standard)
  – L2 Bridge: transparent frame forwarding

## Slide 4: Hardware Assembly
• SAM E54 Curiosity Ultra (red board) + LAN8651 Two-Wire ETH Click (green, eth0) + LAN8740A PHY Daughter Board (bottom left, eth1)

## Slide 5: Physical Layout & Connectors
SAM E54 Curiosity Ultra Development Board (red in photo)
  EDBG on-board debugger (UART debug console)
  GMAC connector for eth1 (100BASE-T to LAN8740A PHY)
  Mikrobus socket for SPI peripheral expansion
LAN8651 Two-Wire ETH Click (green in photo, MIKROE-5543)
  Mounts in Mikrobus socket of SAM E54 board
  SPI master (DIN=MOSI, DOUT=MISO, CLK=SCK, CS=PC15)
  Interrupt pin nIRQ on PC14
LAN8740A PHY Daughter Board (bottom-left in photo, AC320004-3)
  Connects to GMAC interface of SAM E54
  Four twisted-pair Ethernet port (standard RJ45)
Single 10BASE-T1S Cable (Point-to-Point)
  Connects all nodes on the T1S network segment
  Two wires (TX+, TX-) carry all PLCA-coordinated traffic

## Slide 6: Signal Path & Data Flow
T1S Network (point-to-point)
LAN8651 PHY (Receive)
SPI/TC6 Interface
SAM E54 MAC (GMAC)
L2 Bridge Logic
100BASE-T Network
• Frames arrive on eth0 via 10BASE-T1S
• LAN8651 buffers & signals via SPI interrupt (PC14)
• SAM E54 reads frame, learns MAC, forwards to eth1
• GMAC transmits on 100BASE-T; return path mirrors back to T1S

## Slide 7: Key Component Roles
LAN8651 — 10BASE-T1S PHY with PLCA
  Hardware timestamping on RX/TX for PTP (future)
  PLCA slots (contention-free scheduling)
  IEEE test modes (voltage, droop, spectrum, high-Z)
LAN8740A — Standard 100BASE-T PHY
  Multi-pair (four twisted pairs per connection)
  No PLCA — legacy Multi-Master-Slave scheduling
MPLAB Harmony v3 — TCP/IP Stack with L2 Bridge Patches
  Dual-PHY MAC learning & forwarding logic
  Port mirroring (SPAN) support
  Raw frame injection (EtherType bypass)

## Slide 8: Part 2: PLCA — Physical Layer Collision Avoidance

## Slide 9: PLCA Concept — Deterministic Access
Traditional Ethernet (CSMA/CD)
PLCA (IEEE 802.3-2022 Clause 171)
• Carriers sense & listen before transmit
• Collision on multi-drop bus → backoff retry
• Latency unpredictable, varies with load
• Throughput degrades as node count grows
• Coordinator grants time slots to nodes
• Each node waits its turn — zero collisions
• Latency bounded, deterministic
• Ideal for industrial & automotive real-time

## Slide 10: PLCA Parameters & Configuration
Node ID — 0..255
  0 = Coordinator (grants slots, sends beacons)
  1–255 = Regular nodes (wait for slot)
Node Count (CNT) — 1..255
  Number of active nodes on the segment
Slot Time — microseconds per PLCA slot
  Default varies with media (10BASE-T1S: ~40 µs/slot)
Enabled via setenv plca_id <N>; saveenv (persistent)

## Slide 11: Part 3: Functional Features & CLI

## Slide 12: L2 Bridging vs. Port Mirroring — Two Different Functions
Why do we need 'mirror on' if the bridge already forwards traffic?
L2 Bridge (Normal Operation)
Port Mirror (SPAN — Debugging Only)
• Forwards traffic between eth0 ↔ eth1
  – Data frames flow through transparently
  – eth0 frames go to eth1 (and vice versa)
  – Each frame delivered ONCE to destination
• T1S nodes talk to 100BASE-T network — bridge is invisible
  – Use case: normal bridge operation (production)
• COPIES eth0 frames to eth1 for monitoring
  – eth0 traffic is duplicated (not moved)
  – Original bridge forwarding still happens
  – Extra copy sent to Wireshark on the PC
• Analyzer sees T1S bus without physical probe
  – Use case: debugging, compliance testing, bus analysis

## Slide 13: Why Mirror Is Essential for Debugging
The 100BASE-T side (eth1) cannot natively see T1S traffic
  Two different physical media with different PHYs
  Wireshark on the PC plugged into eth1 sees only 100BASE-T frames
To see T1S frames on your PC, the bridge must copy them to eth1
  mirror 1 enables SPAN — copy eth0 → eth1
  mirror 0 disables SPAN — back to normal bridging
Mirror does NOT interfere with the bridge forwarding
  Data flows normally AND gets copied for analysis
  Perfect for seeing T1S bus traffic without stopping the bridge

## Slide 14: Core Bridge Functions
Three independent, complementary capabilities
L2 Forwarding
• Transparent MAC learning
• eth0 ↔ eth1 bidirectional
• PLCA-aware scheduling
• FDB aging (default 5 min)
Port Mirroring (SPAN)
• Copy eth0 → eth1 (SPAN)
• Duplicate, not redirect
• Wireshark capture capable
• Toggleable: mirror 1/0
Raw Frame Testing
• EtherType 0x88B5 bypass
• TCP/IP stack agnostic
• Reproducible timing tests
• noip_send / noip_stat cmds

## Slide 15: Essential CLI Commands — Configuration
# Environment (Persistent in EEPROM)
showenv # Show IP, MAC, PLCA settings
setenv ipaddr 192.168.0.200 # Set eth0 IP (default)
setenv hwaddr 00:1A:2B:3C:4D:5E # Set MAC address
setenv plca_id 0 # Set Node ID (0=Coordinator)
setenv plca_cnt 8 # Set Node Count
saveenv # Persist to EEPROM
readenv # Read from EEPROM (verify)
resetenv # Restore factory defaults

## Slide 16: Essential CLI Commands — Diagnostics
# Bridging & Diagnostics
stats # Real-time counters (RX/TX packets)
meminfo # Heap usage, free memory, watermark
dump 0x20000000 64 # Hex memory dump (64 bytes)
mirror 1 # Enable Port Mirroring
mirror 0 # Disable Port Mirroring
# PHY & Register Access
lan_read 0x000308FB # Read LAN8651 register
lan_write 0x000308FB 0x2000 # Write register value
lan_rmw 0x000308FB 0x7000 0x2000 # Read-Modify-Write

## Slide 17: IEEE Test Modes & PLCA
# Test Modes (IEEE 802.3-2022 §147.5.2)
testmode # Show current mode (0=Normal)
testmode 1 # Test Mode 1 (voltage/jitter)
testmode 1 30 # Mode 1 + auto-revert after 30 s
testmode 2 # Test Mode 2 (droop)
testmode 3 # Test Mode 3 (spectrum)
testmode 4 # Test Mode 4 (high-Z/open circuit)
testmode 0 # Return to normal operation
# PLCA Runtime Control (volatile, lost on reboot)
plca_node # Show current Node ID
plca_node 0 # Become Coordinator
plca_node 7 # Join as regular node #7

## Slide 18: Raw Frame Testing & Network Perf
# Raw Frame Testing (No IP stack)
noip_send 10 2 # Send 10 frames, 2 ms apart (EtherType 0x88B5)
noip_stat # Show frame counters (RX/TX/loss)
# Performance Testing (requires iperf client)
iperf # Start iperf server (default 5001)
iperfk # Stop iperf gracefully
# Help & Discovery
help # List all commands
lanhelp # LAN865x register commands
• noip_send bypasses TCP/IP stack — pure Ethernet measurements
• Useful for latency-sensitive protocols (SOME/IP-SD, CANopen over Ethernet)

## Slide 19: Register Addressing — Memory Map Selector (MMS)
MMS Ranges & Banks
Address Encoding & Examples
• 0x00: OA Standard (config, status)
• 0x01: MAC (Wall Clock, TX-TS)
• 0x02: PHY PCS (link control)
• 0x03: PHY PMA/PMD (test modes, loopback)
• 0x04: PHY Vendor (PLCA, SQI, CFD)
• 0x0A: Misc (1PPS, PADCTRL, DEVID)
• Full = (MMS << 16) | Offset
  – PLCA_CTRL1 = 0x0004CA02
  – MMS 0x04 (Vendor), Offset 0xCA02
  – T1STSTCTL (test modes) = 0x000308FB
  – MMS 0x03 (PMA/PMD), Offset 0x08FB
• ALWAYS verify with lan_read after writes!

## Slide 20: Part 4: Test Modes in Detail

## Slide 21: IEEE 802.3 Test Modes — What & Why
Test Mode 1 (T1STSTCTL = 0x2000)
  Measures: Output voltage, timing jitter, frequency accuracy
  Instrument: Oscilloscope with rise/fall edge detection
Test Mode 2 (0x4000)
  Measures: Output droop (voltage sag under load)
  Instrument: Oscilloscope (zoom on falling edge)
Test Mode 3 (0x6000)
  Measures: PSD spectrum (EMI/RFI compliance)
  Instrument: Spectrum analyzer (1 MHz–1 GHz)
Test Mode 4 (0x8000)
  Transmitter goes high-impedance (open circuit)
  Measures: Bus impedance, cable termination

## Slide 22: Verification & Safety
Always read back after every mode change
  lan_read 0x000308FB verifies the write
  testmode command auto-verifies ([VERIFY] PASS/FAIL)
Safety: T1S link is DOWN during test modes
  Bridge cannot forward traffic during measurement
  Auto-revert prevents accidental lockout (testmode 1 30)
Test modes are transient — revert to 0x0000 when done

## Slide 23: Part 5: Build, Deployment & Troubleshooting

## Slide 24: Build & Flash Workflow
Clone repo → build.bat (generates makefiles + compiles)
  No manual MPLAB-X steps required
  nbproject/Makefile-*.mk auto-generated from .xml
build.bat rebuild for clean rebuild
flash.bat deploys via pyOCD + EDBG probe
  Artifact: firmware/T1S_100BaseT_Bridge.X/dist/…/…hex
Console: EDBG COM port, 115200 8N1 (auto on plug)
  python cli.py --port COM8 --read 1 '<cmd>' to send commands

## Slide 25: Network Setup — IP Addressing Strategy
Bridge Interface IPs (Fixed)
Host PC Configuration
• eth0 (LAN8651): 192.168.0.200
• eth1 (GMAC): 192.168.0.210
• Both in same /24 subnet (no routing)
• Codified in configuration.h (static, DHCP off)
• Persistent over reboot — no re-negotiation
• eth1 adapter → static 192.168.0.100
  – Netmask 255.255.255.0
• Verify with ipconfig or netsh
• Ping tests:
  – ping 192.168.0.200 → eth0 reachable
  – ping 192.168.0.210 → eth1 reachable & forwarding works

## Slide 26: Common Troubleshooting Checklist
Bridge not forwarding frames
  Check: mirror 0 (disable mirroring, test core logic)
  Check: stats (count RX/TX, look for drops)
  Check: test_mirror.py (automated bidirectional test)
PLCA nodes not synchronizing
  Verify: plca_node 0 on one board (Coordinator)
  Verify: plca_node 1–7 on other boards
  Check: test_lan8651.py (auto-verifies PLCA frames flow)
Addresses show (Duplicate) in Windows
  Conflict with 192.168.0.200 or .210 — use .100 on host

## Slide 27: Part 6: Automation & Testing

## Slide 28: Automated Test Suite
test_lan8651.py
  Verifies all four IEEE test modes (Readback, traffic-stops, traffic-resumes)
  Requires: PLCA Coordinator (Node ID 0), python3, pyserial
  Exit code 0 = all modes pass; ≠ 0 = failure (easy CI integration)
test_mirror.py
  Checks Port Mirror bidirectionality (eth0→eth1, eth1→eth0)
  Catches silent failure if DRV_LAN865X_PacketTx hook is missing
cli.py
  Python tool — send CLI commands from scripts, parse responses
  Enables: iperf automation, register sweeps, log collection

## Slide 29: Part 7: Reference & Resources

## Slide 30: Documentation Hierarchy
README.md — Full architecture, setup, iperf examples, FAQs
  Best starting point for new users
LAN8651_TEST_MODES.md — Test mode deep dive
  Measurement setup, example plots, troubleshooting
CLAUDE.md — Firmware implementation notes & fallstricke
  Register quirks, callback pitfalls, PLCA addressing
CLI_COMMANDS.md — Command reference (auto-generated)

## Slide 31: Key Tools & Scripts
build.bat — Compile & link (auto makefiles)
flash.bat — Deploy via pyOCD
cli.py — Send commands over UART, capture responses
test_lan8651.py — IEEE test mode verification
test_mirror.py — Port Mirror bidirectional check
build_summary.py — Flash/RAM usage & interrupt summary

## Slide 32: External Resources
IEEE 802.3-2022 Clause 171 — PLCA specification
IEEE 802.3-2022 Clause 147.5.2 — 10BASE-T1S test modes
LAN8651 Datasheet — PHY register definitions, timing
SAM E54 DS — Memory map, GMAC, SPI, EEPROM
MPLAB Harmony v3 TCP/IP Stack Documentation

## Slide 33: Part 8: Use Cases & Next Steps

## Slide 34: Typical Deployment Scenarios
Industrial Automation — Extend 100BASE-T to single-pair (long cable runs)
  Cost reduction: 4 twisted pairs → 1 pair (cable & connector savings)
  Deterministic PLCA scheduling for motion control
Automotive In-Vehicle Networking — T1S backbone with 100BASE-T gateways
  Mixed-media bridge for legacy & next-gen nodes
Building Automation — T1S branch (energy efficient) to Ethernet backbone
  Low power sensors on T1S; aggregation on 100BASE-T

## Slide 35: Future Enhancements (Out of Scope)
PTP 1588 — IEEE time synchronization (10 µs median tested)
Cyclic Fire — scheduled actions at synchronized timestamps
VLAN support — multiple virtual bridges
QoS — priority queuing per PLCA node
Remote management — SNMP, syslog

## Slide 36: Questions & Next Steps
T1S 100BASE-T Bridge Training — Complete
Microchip Field Application Engineering
2026-08